## Slide 1: Computer Architecture Experiment
Topic 5. Dynamically Scheduled Pipelines using Scoreboarding
浙江大学计算机学院
2024年11月

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of piplines that support multicycle operations.
Master the design methods of piplines that support multicycle operations.
Master verification methods of pipelined CPU supporting multicycle operations.

## Slide 4: Experiment Task
Redesign the pipelines with IF/ID/FU/WB stages and FU stage supporting multicycle operations.
Redesign of CPU Controller.
Verify the Pipelined CPU with program and observe the execution of program.

## Slide 6: Architecture Overview – FU
// FU
FU_ALU alu(...);
FU_mem mem(...);
FU_mul mu(...);
FU_div du(...);
FU_jump ju(...);

## Slide 7: Control Unit
module CtrlUnit(
input clk,
input rst,
input[31:0] inst,
input valid_ID,
input ALU_done,
input MEM_done,
input MUL_done,
input DIV_done,
input JUMP_done,
input cmp_res_FU,
// IF
output reg_IF_en, branch_ctrl,
// ID
output reg_ID_en, reg_ID_flush,
output[2:0] ImmSel,
output ALU_en, MEM_en, MUL_en, DIV_en, JUMP_en,
// FU
output[3:0] JUMP_op,
output[3:0] ALU_op,
output ALUSrcA,
output ALUSrcB,
output MEM_we,
// WB
output reg[2:0] write_sel,
output reg[4:0] rd_ctrl,
output reg reg_write
);

## Slide 8: Function Unit – ALU
module FU_ALU(
input clk, EN,
input[3:0] ALUControl,
input[31:0] ALUA, ALUB,
output[31:0] res,
output zero, overflow,
output finish
);
reg state;
assign finish = state == 1'b1;
initial begin
state = 0;
end
reg[3:0] Control;
reg[31:0] A, B;
always@(posedge clk) begin
if(EN & ~state) begin // state == 0
A <= ...;
B <= ...;
Control <= ...;
state <= 1;
end
else state <= 0;
end

## Slide 9: Function Unit – MUL
module FU_mul(
input clk, EN,
input[31:0] A, B,
output[31:0] res,
output finish
);
reg[6:0] state;
assign finish = state[0] == 1'b1;
initial begin
state = 0;
end
reg[31:0] A_reg, B_reg;
always@(posedge clk) begin
if(EN & ~|state) begin
A_reg ...
B_reg ...
state ...
end
else state <= {1'b0, state[6:1]};
end
wire[63:0] mulres;
multiplier mul(.CLK(clk),.A(A_reg),.B(B_reg),.P(mulres));
assign res = mulres[31:0];
endmodule

## Slide 10: Function Unit – DIV
module FU_div(
input clk, EN,
input[31:0] A, B,
output[31:0] res,
output finish
);
wire res_valid;
wire[63:0] divres;
reg state;
assign finish = res_valid & state;
initial begin
state = 0;
end
reg A_valid, B_valid;
reg[31:0] A_reg, B_reg;
always@(posedge clk) begin
if(EN & ~state) begin // state == 0
A_reg ...
B_reg ...
A_valid ...
B_valid ...
state ...
end
else if(res_valid) begin
A_valid ...
B_valid ...
state ...
end
end
divider div(.aclk(clk),
.s_axis_dividend_tvalid(A_valid),
.s_axis_dividend_tdata(A_reg),
.s_axis_divisor_tvalid(B_valid),
.s_axis_divisor_tdata(B_reg),
.m_axis_dout_tvalid(res_valid),
.m_axis_dout_tdata(divres)
);
assign res = divres[63:32];
endmodule

## Slide 11: Function Unit – JUMP
module FU_jump(
input clk, EN, JALR,
input[2:0] cmp_ctrl,
input[31:0] rs1_data, rs2_data, imm, PC,
output[31:0] PC_jump, PC_wb,
output cmp_res, finish
);
reg state;
assign finish = state == 1'b1;
initial begin
state = 0;
end
reg JALR_reg;
reg[2:0] cmp_ctrl_reg;
reg[31:0] rs1_data_reg, rs2_data_reg, imm_reg, PC_reg;
always@(posedge clk) begin
if(EN & ~state) begin // state == 0
JALR_reg ...
cmp_ctrl_reg ...
rs1_data_reg ...
rs2_data_reg ...
imm_reg ...
PC_reg ...
state ...
end
else state ...
end
cmp_32 cmp ...
add_32 a...
add_32 b...
endmodule

## Slide 12: Function Unit – MEM
module FU_mem(
input clk, EN, mem_w,
input[2:0] bhw,
input[31:0] rs1_data, rs2_data, imm,
output[31:0] mem_data,
output finish
);
reg[1:0] state;
assign finish = state[0] == 1'b1;
initial begin
state = 0;
end
reg mem_w_reg;
reg[2:0] bhw_reg;
reg[31:0] rs1_data_reg, rs2_data_reg, imm_reg;
always@(posedge clk) begin
if(EN & ~|state) begin
mem_w_reg ...
bhw_reg ...
rs1_data_reg ...
rs2_data_reg ...
imm_reg ...
state ...
end
else state ...
end
wire[31:0] addr;
add_32 add...
RAM_B ram(.clka(clk),.addra(addr),.dina(rs2_data_reg),.wea(mem_w_reg),
.douta(mem_data),.mem_u_b_h_w(bhw_reg));
endmodule

## Slide 13: Pipelines resolving Data Hazards
Stall the pipeline to deal with data hazard!

## Slide 14: Pipelines resolving Control Hazards
Predict-not-taken
Condition and Addr. Calculation in FU

## Slide 15: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | 
3 | 004100b3 | C |  | add x1, x2, x4 | 
4 | fff08193 | 10 |  | addi x3, x1, -1 | 
5 | 00c02283 | 14 |  | lw x5, 12(x0) | 
6 | 01002303 | 18 |  | lw x6, 16(x0) | 
7 | 01402383 | 1C |  | lw x7, 20(x0) | 
8 | 40220433 | 20 |  | sub x8,x4,x2 | 
9 | ffd50493 | 24 |  | addi x9,x10,-3 | 
10 | 00520c63 | 28 |  | beq x4,x5,label0 | 
11 | 00420a63 | 2C |  | beq x4,x4,label0 | 
12 | 03000a13 | 30 |  | addi x20,x0,48 | 
13 | 03400a13 | 34 |  | addi x20,x0,52 | 
14 | 03800a13 | 38 |  | addi x20,x0,56 | 

## Slide 16: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 03c00a13 | 3C |  | addi x20,x0,60 | 
16 | 00004537 | 40 | label0: | lui x10,4 | 
17 | 014005ef | 44 |  | jal x11,20 | 
18 | 04800a13 | 48 |  | addi x20,x0,72 | 
19 | 04c00a13 | 4C |  | addi x20,x0,76 | 
20 | 05000a13 | 50 |  | addi x20,x0,80 | 
21 | 05400a13 | 54 |  | addi x20,x0,84 | 
22 | ffff0617 | 58 |  | auipc x12, 0xffff0 | 
23 | 0223c6b3 | 5C |  | div x13, x7, x2 | 
24 | 02520733 | 60 |  | mul x14, x4, x5 | 
25 | 022687b3 | 64 |  | mul x15, x13, x2 | 
26 | 00400813 | 68 |  | addi x16, x0, 4 | 
27 | 000008e7 | 6C |  | jalr x17,0(x0) | 

## Slide 17: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 18: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;

## Slide 19: Simulation

## Slide 20: Simulation

## Slide 21: Simulation
IF
ID
FU

## Slide 22: Simulation

## Slide 23: Simulation
Next FU EN
WB

## Slide 24: Simulation

## Slide 25: Simulation

## Slide 26: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 27
Thanks!